## Slide 1
Scenario and control modeling for development of DD low-activation ITER operation
ITPA IOS meeting
October 18 – 21, 2011
Kyoto, Japan
T. A. Casper, D. Campbell, Y. Gribov, A. Polevoi and J.A. Snipes
ITER Organization, Route de Vinon sur Verdon, 13115 St Paul Lez Durance, France

## Slide 2: A “low activation” scenario for early ITER operation: a controllable scenario with acceptable tritium production?
Operation at half plasma current, IP=7.5MA, and half toroidal magnetic field BT=2.65T with the JCT-2001 controller
Explore issues with early DD operations: performance and activation
15MA inductive case re-defined for 7.5MA study
  Same input waveforms – except early heating not required for PF/CS limits and do want to pre-heat neutron flux
  Same shapes – inside wall limited and full plasma shape
  Assume H-mode access with auxiliary heating, Paux
Initial scenario developed: D as base particle source, T from reaction rates:
    DDn: D+DHe3+n0 at ~50%
    DDp: D+DT+p+ at ~50% - tritium source rate
    DT: D+THe4+n0 produced T burn up
    ST: DDp – DT resulting T particle source rate  NT(f)
  Assume no T diffusion (perfect confinement) to calculate maximum production
  Auxiliary heating power and transport assumptions varied
  Analytic sources and density profiles for development so far

## Slide 3: DD operation: long pulse preceding DT operation and “possible” short pulse for early operations
D Low-activation long pulse case: IP=7.5MA and BT=2.65T (half IP, BT)
  Candidate for early ITER operation under development
    Hydrogen may not make long pulse H-mode, e.g. L-to-H threshold too high
  Concern for tritium production
    Activation/licensing may limit duration
  Use electron heating only
    Suppose NBI are not available
  Interested in lower current at full field: 10MA, 12MA – no work done
Short pulse D operations rather than H or He to investigate ELM control
  Purely “what if” for now – “the Regulator” says no D operation in “non-active” phase
  So “not likely” now since it will have to be introduced later in licensing – several of these expected
  Must be low activation, so likely 10 to 20 second flattop
Non-activation: H or He operations at reduced IP, BT are main candidates

## Slide 4: Simulation with Paux=53MW of electron heating results in T particle inventory of 0.3x1020 after a 400s flattop pulse
(a) Plasma current and auxiliary heating power
  Resulting electron and ion temperatures at the magnetic axis using the C-T thermal transport model
(b) On-axis electron density assumed (peak in NGW=.51x1020
  Tritium density from reaction rate source: NT~ND/400
  Resulting alpha heating Palpha ~ Paux/500
  Internal inductance evolution, li3, vertical stability parameter
  Confinement, h98y2, from scaling of C-T model
(c) Rates for nuclear reactions
  ---------- volume-integrated rate in #/s
  *---*---* time-integrated accumulations in #
  S is the T particle source: at t = 500s, the total integrated T production is ~ .3x1020 particles ~ .15mg

## Slide 5: Assumed and simulated profiles at 450s for flat-top current of IP=7.5MA with Paux=53MW
(a) Input density profiles
  Ne assumed H-mode electron density profile shape (same as 15MA inductive modeling)
  ND is the assumed deuterium
  qimp*Nimp is the charge-scaled (e.g. fully ionized) impurity assumed to be carbon at NC/ND = .055  Zeff=1.7
  NT is the resulting tritium density profile resulting from the T-particle reaction source rate: NT ~ ND/400
(b) Response profiles using the C-T transport model
  Temperature profiles, Te and Ti
  <JT.B>/<BT/R> is the total flux-surface-averaged current – sawtooth flattening
  Safety factor, q

## Slide 6: Reaction rates for plasma parameter scans indicates the weak scaling of tritium buildup
Volume integrated rates - particles/s Total integrated source - particles

## Slide 7: Free-boundary evolution with JCT2001+VS1 controller (from 15MA inductive scenario) maintains plasma shape and vertical position
(a) CS and (b) PF coil currents which are far from allowed limits
(c) CS and (d) PF voltages for feedback control of plasma shape
(e) Fast voltage applied to PF2-PF5 coils for VS1 control of vertical position

## Slide 8: Controller capable of making the transition from inside-wall limited to diverted shapes – shape/position control needs to be optimized
Modification of strike point to pull shape off inside wall
Modification of upper control gap to eliminate poor shape control at full IP

## Slide 9: Summary: We have developed a DD scenario for early ITER operation and estimated the tritium production
Developed and initial scenario for operation of ITER at BT/2=2.65T and IP/2=7.5MA with the same assumptions for transport as the 15MA inductive
Simulated control of this scenario was demonstrated was demonstrated with the JCT-2001 controller + VS1 for vertical position
  Coil currents and forces are within allowed limits
Estimates of the resulting buildup of tritium give.3x1020 particles per full 400s duration flattop: 0.15mg or .55x105MBq reactivity
Tritium buildup – select reactivity desired
  weak function of the heating power (for assumed confinement)
  approximately linear with pulse duration
Additional work planned:
  Compare with other estimates of tritium production
  Turn on transport of produced tritium to develop a true scenario
  Source modeling
  Operational space